Installation of the MagicBullettm

Proper installation of the MagicBullettm is quick and simple. Simply unplug the Ethernet cable from the radio to be protected and insert the Ethernet cable on the MagicBullettm into the now empty Ethernet jack on the radio.

Remove the bottom of the MagicBullettm (pressed on fit) by gripping the top cap and pulling down to the bottom section. Twisting the bottom section will loosen, if needed.

Take the end of the Ethernet cable you removed from the radio and feed it through the bottom cable grommet on the MagicBullettm ; feed it up through the bottom and into the Ethernet jack on the bottom of the MagicBullettm PCB. Slide the bottom of the MagicBullettm up into the top section and press it in firmly. You may use a small amount of silicone sealant or coax seal to help secure the top and bottom sections together.

Take two black zip ties and secure the MagicBullettm to the mast or tower leg as shown in the example photo below. This will help insure the MagicBullettm's top and bottom halves remain together and also prevent wind from blowing the MagicBullettm and fatiguing the cable. It's important the MagicBullettm be mounted vertically with no more than around 15 degree of tilt.